## Slide 1
Personalized Deep Learning Model for Closed-Loop 40 Hz Entrainment to Optimize Theta-Gamma Coupling in Alzheimer's Disease
Amaar M. Chughtai
INTRODUCTION
Alzheimer's disease affects 55 million people worldwide with no cure. Emerging research shows 40 Hz auditory stimulation drives gamma brain rhythms that promote clearance of toxic amyloid-β plaques through microglial activation and glymphatic fluid exchange (Iaccarino et al., 2016; Murdock et al., 2024).
Current clinical protocols deliver stimulation on a fixed schedule — the same for every patient. This ignores two critical problems:
  ~30% of patients habituate within minutes (Fortunato et al., 2023)
  Responding patients still lose entrainment periodically, wasting stimulation during strong coupling and missing periods of genuine need
[FIGURE: Fixed vs. Adaptive comparison diagram]
Research Question
Can deep learning models forecast theta-gamma PAC dynamics 5–10 seconds into the future, and does integrating such forecasts into a closed-loop controller improve personalized 40 Hz entrainment therapy?
Hypothesis
A causal TCN can forecast PAC at horizons beyond 3 seconds where simpler baselines fail, and integrating these forecasts into a closed-loop controller will outperform reactive threshold control.
SYSTEM ARCHITECTURE
[INSERT: System architecture diagram — Figure 1] Use results/figures/system_block_diagram.png or the author-generated diagram from the presentation. EEG → Preprocessing → EEGNet (1,457 params) → PAC Estimate → 12-Feature Extraction → Causal TCN (22,914 params, 5s horizon) → Controller (z-score ±0.5, 5s hysteresis) → STIMULATE / REST / MAINTAIN → 40 Hz Audio
KEY DISCOVERY
Dropping 61 spectral features and keeping only 12 PAC-trajectory and stimulation-context features raised test R² from −0.025 to 0.606 (5-seed mean ± 0.032). Spectral features encoded patient-specific anatomy, not generalizable dynamics. Feature selection mattered more than model architecture — 8 architectures all converged at R² = 0.287 on spectral features.
METHODS
Dataset
  OpenNeuro ds005048 (Lahijanian et al., 2024)
  35 elderly subjects: 17 AD, 6 MCI, 10 controls
  7 frontal EEG channels (Fp1, Fp2, F7, F3, Fz, F4, F8)
  250 Hz sampling rate
  Protocol: 40 Hz auditory stimulation (40s ON / 20s OFF)
Preprocessing
  Bandpass: 0.5–80 Hz (4th-order Butterworth, zero-phase)
  Notch: 50 Hz (Q = 30) for power-line removal
  Artifact rejection: ±100 µV threshold
  Common average reference
  2-second windows (500 samples), 1-second hop
PAC Computation
  Modulation Index (Tort et al., 2010)
  Theta phase (4–8 Hz) × gamma amplitude (38–42 Hz)
  KL divergence over 18 phase bins (20°)
  Computed at epoch level (20–40s blocks)
Model
  MultiscaleCausalTCN: 22,914 parameters
  4 causal depthwise-separable conv blocks
  Dilations [1, 2, 4, 8], receptive field = 31 steps
  GroupNorm + SiLU, attention pooling
  Huber loss, AdamW, early stopping (patience = 20)
  12 input features: 7 PAC-derived + 5 stim context
Data Splits (subject-level, no leakage)
  Train: 24 subjects (11,736 windows)
  Validation: 5 subjects (2,725 windows)
  Test: 6 subjects (2,822 windows)
Validation
  Offline counterfactual replay on all 35 subjects
  Ground-truth PAC labels used as TCN input
  6 controller variants compared incl. oracle
  Wilcoxon signed-rank, Hedges’ g, BCa bootstrap CIs
RESULTS
[INSERT: Figure 2 — Controller Comparison Bar Chart] Use results/figures/controller_comparison.png Resize to fill ~11" x 4.2" in this box Shows all 6 controllers: Fixed, PI, Reactive, TCN, Hybrid, Oracle across Alignment, Low-PAC Stim Rate, High-PAC Rest Rate
Figure 2. Controller comparison on 35 subjects’ real EEG. TCN achieves 72.1% alignment vs 64.5% reactive (g = 1.31, p < 0.001).
[INSERT: Figure 3 — Horizon Sweep] results/figures/horizon_sweep.png R² across 1–10s horizons TCN maintains 0.37–0.67 Baselines collapse beyond 3s
[INSERT: Figure 4 — Per-Subject Scatter] results/figures/per_subject_utility.png All 35 dots above diagonal Train/Val/Test splits marked Binomial p < 0.001
72.1%
Alignment
vs 64.5% reactive g = 1.31, p < 0.001
82.6%
Low-PAC Targeting
vs 51.7% reactive g = 4.47, p < 0.001
35 / 35
Subjects Benefited
binomial p < 0.001 91% of oracle gap
The predictive controller reaches 91% of the theoretical oracle’s targeting gap, demonstrating that 5-second PAC forecasting enables personalized therapy outperforming both fixed and reactive protocols.
CONCLUSIONS & FUTURE DIRECTIONS
Conclusions
  The predictive controller reaches 91% of the theoretical oracle’s targeting gap across all 35 subjects
  Feature selection was the breakthrough: 12 PAC-trajectory features outperform 73 spectral features five-fold (R² = 0.606 vs. −0.025)
  Eight neural network architectures (1,457 to 1.1M params) all converged at R² = 0.287 on spectral features — the bottleneck was data representation, not model capacity
  The TCN maintains R² = 0.37–0.67 at 3–10s horizons where all baselines collapse to negative R²
  All 35 subjects benefited, including 6 held-out test subjects never seen during training
  Advantage is robust across z-score thresholds 0.2–1.0 and four fatigue model assumptions
Statistical Validation
TCN vs. Reactive Threshold (N = 35, paired):
Alignment: g = 1.31 [0.75, 1.87] p < 0.001
Low-PAC targeting: g = 4.47 [3.33, 5.62] p < 0.001
PAC Gap: g = 1.57 [0.98, 2.17] p < 0.001
  Wilcoxon signed-rank tests (non-parametric, paired)
  Hedges’ g with 95% BCa bootstrap CIs (10,000 iterations)
  5-seed TCN validation: R² = 0.606 ± 0.032 (range 0.558–0.647)
Future Directions
  Deploy with live EEG streaming for real-time closed-loop validation
  IRB-approved observational pilot at regional memory care facilities (N = 5–10)
  Crossover feasibility study: adaptive vs. fixed stimulation with cognitive outcome measures
  Complete system cost under $250 per patient (consumer EEG headset + standard headphones)
  Extend to multi-biomarker control (PAC + spectral power + connectivity)
Broader Impact
The closed-loop control framework generalizes beyond 40 Hz entrainment. The principle — using a biomarker forecast to time interventions proactively — applies to any brain stimulation paradigm where response is variable and predictable. Adaptive DBS for Parkinson’s disease, FDA-approved in February 2025, validates this approach in a different modality.
ACKNOWLEDGEMENTS & REFERENCES
Acknowledgements
My AP Statistics teacher was consulted on statistical test selection. All other work — literature review, software development, experimental design, and analysis — was conducted independently.
Computing: personal Apple Silicon MacBook and personal RTX 3080 GPU. No institutional lab, university mentor, or summer research program was used.
Data: OpenNeuro ds005048, used under open access license.
All diagrams created by the author unless otherwise noted.
References
[1] Iaccarino HG et al. Gamma frequency entrainment attenuates amyloid load. Nature 540, 230–235, 2016.
[2] Murdock MH et al. Multisensory gamma stimulation promotes glymphatic clearance. Nature 627, 149–156, 2024.
[3] Chan D et al. Gamma sensory stimulation in mild Alzheimer’s dementia: open-label extension. Alzheimer’s & Dementia 21(10), e70792, 2025.
[4] Fortunato C et al. Gamma entrainment for cognitive improvement in neurodegeneration. Front Neurosci 17, 2023.
[5] Lahijanian B et al. Auditory gamma entrainment enhances DMN connectivity in dementia. Sci Rep 14, 2024.
[6] Lawhern VJ et al. EEGNet: compact CNN for EEG-based BCIs. J Neural Eng 15, 056013, 2018.
[7] Tort ABL et al. Measuring phase-amplitude coupling. J Neurophysiol 104, 1195–1210, 2010.
[8] Rosin B et al. Closed-loop DBS for Parkinson’s disease. Neuron 72, 370–384, 2011.
California Science and Engineering Fair 2026 • Medicine & Physiology